## Slide 1
Perennial river
Intermittent river
Ephemeral river
river
Navigable Water Protection Rule 2020:
“[Regulated] surface water channels must flow more often than just after a single precipitation event—that is, tributaries must be perennial or intermittent”

## Slide 2: Problems with gage-based modeling
Bias in gage locations, particularly w.r.t. to non-perennial streams
  Krabbenhoft et al 2022
VERY few gauges are truly ephemeral (i.e. no baseflow) meaning data-driven modeling is nearly impossible
  I did a hydrograph separation on ~7,000 streamgauges and 53 had 0 baseflow
  Could serve as verification data, but not enough to train an ML model

## Slide 3: Alternative approach to gauge-based modeling
Compare water table depths to the NHD
Fan et al 2017; 2013 global water table depth map!
  Full soil water balance at 1km resolution forced by atmospheric/ecohydrological observations
    Yields mean monthly water table depths
Calibrated/validated in North America using 1,000,000+ well depth measurements

## Slide 4: Water table depths

## Slide 5
Is Water Table Depth
< -1.12m?
Is upstream river perennial?
Yes
No
Perennial river
Is this true all 12 months?
Yes
No
Intermittent river
Yes
No
Ephemeral river
1) threshold for ‘persistent surface saturation’ (Fan 2013): -0.25m
2) average model error across two forcings: -0.867m [Fan etal 2013]
(currently using median along reach, but ideally would run both max and min as upper/lower limits)

## Slide 6: HUC4 river map low example
(size by stream order)
HUC 1104 | % Q | % surface area
Ephemeral | 3% | 93%
Intermittent | 2% | 6.9%
Perennial | 95% | 0.1%
Arkansas River